## Slide 1
SMART INDIA HACKATHON 2026
    Problem Statement ID – SIH26085
    Problem Statement Title- Street-Level Urban Flood Nowcasting (0–3 h) coupling Rainfall, Terrain and Drainage with Flood-Safe Routing
    Theme- Disaster Management
    PS Category- Software
    Team ID- 171929
    Team Name (Registered on portal)- LLMao
1
1
Notes: Team LLMao, problem statement SIH26085. Our solution is Drishti: it tells a city where water will stand on its streets up to three hours before it does, how sure we are, why, and what to do about it.

## Slide 2
LLMao
2
Drishti — Urban Flood Digital Twin
KNOW WHERE THE WATER WILL STAND — THREE HOURS BEFORE IT DOES
0–3 h street-level forecasts • Physics + AI, not AI alone • Piloted on KIET campus, Ghaziabad
OBSERVE
RAIN
Radar, rain gauges,
GPM-IMERG feeds
QUALITY
CONTROL
Every reading tagged
VALID / STALE / FAULT
ENSEMBLE
NOWCAST
20 possible rain
futures, 0–180 min
PHYSICS
DIGITAL TWIN
1D drains + 2D streets,
mass-conserving
AI FLOOD
SURROGATE
U-Net (ONNX) predicts
depth in 0.2 s
DECIDE
& ACT
Hotspots, road status,
safe routes, alerts
CLOSED LOOP — Observe → quality-check → forecast → warn → act → observe again, every 5 minutes, every number labelled.
FIVE QUESTIONS — ONE OPERATOR SCREEN
Every flood decision reduces to five questions. Drishti answers each with a number and a confidence.
WHERE? — street-by-street flood map on a 5 m grid
WHEN? — time-to-10 cm and peak time for every road
HOW BAD? — P10 / P50 / P90 depth, duration, extent
WHY? — rain vs terrain vs drain surcharge vs blockage
WHAT NOW? — ranked actions + 3 alternative routes
0–180 min forecast horizon
5 m street-level grid
DRAINAGE HEALTH WATCHDOG
The twin compares what the drains should do with what sensors see — and names the likely culprit.
Hidden blockages found
Residuals ranked pipe P-49 as likely blocked — it was one of 2 hidden blockages
Faulty sensors isolated
Stuck sensor S-27 drops to trust 0.28 and is ignored; the twin keeps running
Forecast corrected by live sensors
Kalman update cuts sensor-level error from 19.9 cm to 2.7 cm
Recommend, never auto-control
Work orders and actions wait for a human to approve them
DEGRADED-MODE HONESTY
Radar lost? Falls back to gauges, widens uncertainty and shows DEGRADED — never silently guesses.
19 s full forecast cycle
67% cells warned in time
Notes: Drishti is a digital twin of the campus drainage and streets. Rain is observed, quality-checked, turned into 20 possible rain futures, pushed through a physics model and a fast AI copy of it, and ends as decisions: which streets flood, when, how badly, why, and what to do. The loop repeats every 5 minutes. It also diagnoses the drains themselves and is honest when data fails. Numbers are from synthetic twin experiments (Level-1 demo data).

## Slide 3
LLMao
TECHNICAL APPROACH
CONFIG-DRIVEN · YAML · ONE REPO
PROVENANCE · LABELS · 31 TESTS
PYTHON · NUMPY PHYSICS CORE
PART 01
TERRAIN TWIN
PART 02
COUPLED PHYSICS
PART 03
FORECAST ENGINE
PART 04
CLOSED LOOP
PART 05
DECISIONS · ALERTS · API
DATA SOURCES
Copernicus DEM
OpenStreetMap
GPM-IMERG
Radar (MOSDAC)
NumPy · SciPy
PyTorch
ONNX Runtime
HDF5
MapLibre GL
Three.js
Chart.js
pytest
YAML config
Vercel static
U-Net
residual · 270k params
36 inputs
rain · depth · terrain
14 leads
5 → 180 min
0.2 s
ONNX · 1 MB
1
290 PHYSICS
STORM RUNS
2
6,448
WINDOWS
3
TRAIN
12 EPOCHS
4
EXPORT
TO ONNX
5
SCORE vs
PERSISTENCE
CSI 0.79 vs 0.24 persistence at +180 min
SYNTHETIC DRAINS
LABELLED
30 m DEM TIER
SHOWN IN UI
NO ROUTE EVER
CALLED 'SAFE'
PROVENANCE · LOGGED ON EVERY STEP
RAIN OBSERVATIONS
QUALITY CHECK
FAULT → REJECTED
RADAR USABLE?
GAUGES ONLY
= DEGRADED
ENSEMBLE NOWCAST
20 MEMBERS
TWIN STATE AT t₀
AI SURROGATE DEPTHS
HOTSPOT RISK?
FULL PHYSICS
REFINE
PROBABILISTIC FORECAST
P10 · P50
· P90
CROSSES 10 cm?
EARLY
WARNING
IMPACT · ROUTES · ALERT
AUDIT LEDGER
YES
DEM
FILL SINKS
D8 FLOW
LOW POINTS
OSM LAYERS
DRAIN GRAPH
SWMM .inp
WHY HYBRID?
Full physics × 20 members ≈ 4 min
AI surrogate × 20 members ≈ 0.2 s
Physics re-runs only hotspots → 19 s
RAIN
FIELD
HORTON
SCS-CN
2D
SURFACE
INLET
EXCHANGE
1D PIPES
& PUMPS
Weir / orifice exchange · surcharge returns to the street · mass balance ~1e-8
9 VIRTUAL
SENSORS
KALMAN
UPDATE
FAULT
ISOLATION
BLOCKAGE
DIAGNOSIS
OPTICAL
FLOW
FFT CASCADE
AR(2)
NOISE
× 20
NWP
BLEND
CAP 1.2
ALERTS
REST API
· GeoJSON
RBAC
· 6 ROLES
1
SYSTEM ARCHITECTURE
2
AI FLOOD SURROGATE
3
DATA HONESTY
4
FORECAST CYCLE — EVERY 5 MINUTES
5
TERRAIN & DRAIN NETWORK BUILD
6
COUPLED 1D / 2D PHYSICS
7
CLOSED-LOOP DATA ASSIMILATION
ERROR 19.9 → 2.7 cm
8
STEPS RAIN NOWCAST
9
PLATFORM & INTEGRATION
Notes: Left: the codebase is one Python repo — terrain twin, coupled physics, forecast engine, closed-loop twin and decisions — fed by Copernicus DEM, OpenStreetMap and rainfall feeds. Centre: one forecast cycle. Rain is ingested and quality-checked; if radar is unusable we drop to gauges and say DEGRADED; STEPS makes 20 rain futures; the twin state at t0 is propagated by the AI surrogate; hotspots are re-run in full physics; the result becomes P10/P50/P90 maps, early warnings, road impact, routes and alerts. Right: the physics chain, sensor data assimilation, the STEPS algorithm and the integration layer.

## Slide 4
4
LLMao
ONE CAMPUS / CITY WARD · INDICATIVE ESTIMATE
COMPUTE
₹1–1.5 L
SENSORS
₹3–5 L
DRAIN SURVEY
₹2–4 L
SUPPORT / YR
₹1–2 L
WHERE YOUR MONEY GOES
Chart: 
| Sensors | Drain survey | Support | Compute
Share | 0.41 | 0.31 | 0.15 | 0.13
Sensors & gauges
41%
Drain survey
31%
Support / yr
15%
Compute server
13%
Licences
₹0
OPEN DATA
NO LICENCE FEES
₹0
GPU / CLOUD BILL
PER FORECAST
FORECAST SKILL — CSI at 10 cm depth, held-out storms
Drishti AI
Persistence
higher = better
Chart: 
| +30 min | +60 min | +120 min | +180 min
Drishti AI | 0.82 | 0.8 | 0.79 | 0.79
Persistence | 0.58 | 0.39 | 0.26 | 0.24
Python
PyTorch
ONNX
MapLibre
Vercel
TECHNICAL
LAPTOP CPU · NO GPU NEEDED
OPERATIONAL
19 s CYCLE · 60 s BUDGET
ECONOMIC
OPEN DATA · ₹0 LICENCES
REGULATORY
CAP 1.2 · NDMA ALIGNED
$ python -m forecast.run --t0 115 → cycle 19 s
✓ OPERATIONAL
READINESS — self-assessed, out of 100
Technical
90
Operational
80
Economic
88
Regulatory
78
THE RISK IS REAL — wettest day each year, Ghaziabad (mm), from the repo's 10-year record
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Max daily rain (mm) | 114.6 | 90.7 | 66.9 | 66.8 | 76.5 | 102 | 59.6 | 61.7 | 56.7
POLICY IS ON OUR SIDE
NDMA URBAN FLOOD GUIDELINES
NOTHING TO REWRITE
SURVEYED DRAINS DROP IN
THE NEXT CITY IS A CONFIG
1 → N WARDS
ALREADY ON DISK
290
physics storm runs, 6 h each, for training
1e-8
typical mass-balance error per run
31
automated tests passing (1 skipped)
THE CHALLENGE
HOW IT IS MITIGATED — IN CODE
NO DRAIN MAP
SYNTHETIC NETWORK, verified=false
SURVEY DATA DROPS IN, SAME SCHEMA
COARSE 30 m TERRAIN
DATA TIER SHOWN IN THE UI
LiDAR / DRONE DEM READY TO SWAP
RADAR CAN GO DOWN
GAUGE FALLBACK, FLAGGED DEGRADED
UNCERTAINTY WIDENED × 1.5
NO FLOOD OBSERVATIONS
TWIN EXPERIMENTS vs HIDDEN TRUTH
REPLAY & VALIDATION VIEW
1
ECONOMICS — COST TO DEPLOY
INDICATIVE
2
FEASIBILITY
RUNNING TODAY
3
VIABILITY
4
CHALLENGES AND MITIGATION
ALL FOUR ANSWERED IN CODE
Notes: Economics: an indicative deployment for one campus or ward is dominated by sensors and a drain survey; software, data and licences cost nothing and the forecast runs on a CPU. The AI surrogate beats the persistence baseline at every lead time. Feasibility: it runs today, a full cycle in about 19 seconds. Viability: the repo's 10-year rainfall record shows 57–115 mm days every year. Challenges: every data gap is labelled and has a drop-in upgrade path.

## Slide 5
LLMao
5
Impacts And Benefits
PUBLIC SAFETY
Citizens are warned street by street before water crosses ankle depth — not after the road is gone.
67% OF CELLS WARNED IN TIME
EMERGENCY RESPONSE
Ambulance and fire routes are checked against the water expected when the vehicle actually arrives.
5 VEHICLE CLASSES · 3 ROUTES
INFRASTRUCTURE HEALTH
Hidden drain blockages and faulty sensors are flagged with evidence, so crews fix the right pipe first.
HIDDEN BLOCKAGE P-49 FOUND
GOVERNANCE & TRUST
Every forecast stores its inputs, model and config — any alert can be replayed and audited later.
EVERY RUN REPLAYABLE
PLANNING & RESILIENCE
What-if runs (rain +20%, pump failure, river backwater) show which fix cuts flooding the most.
5 WHAT-IFS · 3 ACTIONS TESTED
IMPACT & BENEFIT FLOW
1. Rain Observed
Radar + gauges, every
reading quality-checked
2. 3-Hour Forecast
20 possible futures,
P10 / P50 / P90 depth
3. Hotspot Warned
Up to 50 min before water
crosses 10 cm
4. Human-Approved Action
Routes diverted, crews sent,
pumps started
5. Audit & Learn
Sensors correct the twin;
every run replayable
LEAD TIME GAINED
Streets flagged a median 20–50 min before they cross 10 cm, in replayed storms.
FEWER FALSE ALARMS
2% false alarms at the T+115 forecast — warnings people keep trusting.
SMARTER DRAIN SPENDING
Action lab tests pump vs. drain-clearing in physics before money is spent.
LOW COST TO RUN
A full cycle runs on a laptop CPU in ~19 s — no GPU or per-query cloud bill.
SDG 11 & SENDAI ALIGNED
Local early warning that serves SDG 11.5 and the Sendai Framework targets.
WORKS WHEN DATA FAILS
Radar outage? A gauge-only forecast, clearly flagged DEGRADED — never silent.
Notes: Top: five kinds of impact — public safety, emergency response, infrastructure health, governance and planning. Middle: the benefit chain from rain to an audited, human-approved action. Bottom: the measurable benefits. Lead time and false-alarm figures come from replayed synthetic storms against the hidden truth, not from observed floods.

## Slide 6
LLMao
6
Research and References
URBAN FLOOD HYDRAULICS
LISFLOOD-FP: storage-cell 2D flood model
Bates & De Roo, J. Hydrology 236, 2000
Diffusive-wave raster model — the basis of our 2D street-surface solver.
View source →
SWMM 5 Reference Manual, Vol. II Hydraulics
Rossman, US EPA 600/R-17/111, 2017
Node-link sewer hydraulics and surcharge; our 1D network exports to .inp.
View source →
PROBABILISTIC RAIN NOWCASTING
STEPS: short-term ensemble prediction
Bowler, Pierce & Seed, QJRMS 132, 2006
Cascade + stochastic-noise ensembles; our 20-member nowcast follows it.
View source →
pysteps: open-source probabilistic nowcasting
Pulkkinen et al., Geosci. Model Dev. 12, 2019
Reference implementation our NumPy STEPS mirrors: optical flow, AR(2), blending.
View source →
AI SURROGATES & DATA ASSIMILATION
U-Net: convolutional networks for segmentation
Ronneberger et al., MICCAI 2015
Encoder–decoder with skip links; our residual flood surrogate is a U-Net.
View source →
The Ensemble Kalman Filter
Evensen, J. Geophys. Res. 99(C5), 1994
Sequential data assimilation — basis of the twin's sensor correction.
View source →
POLICY, DATA & STANDARDS
NDMA Guidelines: Management of Urban Flooding
National Disaster Management Authority, 2010
Calls for local early warning and drain inventories.
View source →
Copernicus DEM GLO-30
ESA / DLR / Airbus, 2021
30 m global surface model — the KIET twin's terrain.
View source →
DEFENSE IN DEPTH — HOW A FORECAST EARNS TRUST
PHYSICS
DATA
FORECAST
PHYSICS — Mass-conserving twin
Rain in = water out + stored, to ~1e-8; 31 tests guard it.
DATA — Quality & trust scores
Every gauge and radar frame is QC'd; faulty ones are dropped.
FORECAST — Honest probability
P10–P90 bands, DEGRADED flags, no route called 'safe'.
TECHNOLOGY & STANDARDS
ONNX Runtime
Official docs →
MapLibre GL
Official docs →
OpenStreetMap
Official docs →
OASIS CAP 1.2
Official docs →
APPLICATION & VIDEO LINK
LIVE DASHBOARD ↗
3D STORM REPLAY ↗
EXPLAINER VIDEO ↗
SOURCE CODE ↗
github.com/arpitpandey0307
Notes: Every method in Drishti traces to published work: LISFLOOD-FP and SWMM for hydraulics, STEPS and pysteps for rain nowcasting, U-Net for the surrogate, the Ensemble Kalman Filter for assimilation, and NDMA's urban flooding guidelines for the operational need. Links at the bottom open the live dashboard, the 3D replay, the explainer video and the source code.